## Slide 1: GDA – IEC 61970-403
GDA permits a client to access data maintained by another component (either an application or database) or system without any knowledge of the logical schema used for internal storage of the data. Knowledge of the existence of the common model is sufficient.
GDA standard describes two forms for GDA read access. The first, originally standardized within the OMG as the Utility Management System (UMS) Data Access Facility (DAF), provides clients a basic ability to query for instance data and metadata (Resource query module). The second extends UMS DAF to provide clients a more advanced ability whereby clients can perform more advanced query filtering and joining (Filtered query module and Extended query module ).
The idea is to represent any class and its attribute from an internal model with unique model codes, adhering to specific rules
Notes: IEC 61970-403 Ed.1: Energy management system application program interface
(EMS-API) - Part 403: Generic data access
This standard is one of the IEC 61970 series parts that define services for utility operational
systems.
The IEC 61970-4xx series specifies a set of interfaces that a component (or application) should
implement to be able to exchange information with other components and/or access publicly
available data in a standard way. The 61970-4xx series component interfaces describe the
specific event types and message
IEC 61970-403 Generic Data Access (GDA) defines services that are needed to access public
entity objects for the power system domain that are defined in the IEC 61970-3xx series:
Common Information Model (CIM). GDA permits a client to access data maintained by another
component (either an application or database) or system without any knowledge of the logical
schema used for internal storage of the data. Knowledge of the existence of the common
model is sufficient.

## Slide 2: GDA Concepts
The DAF and GDA formulate queries and their results in terms of resources, properties, and values. For example, the simplest query asks for the values of several properties of a given resource.
Resource
  A resource is any object identified with a distinct identifier.
Property
  A property is some aspect of a resource that can be described. For example, location and operation-count could be properties of a switch. When properties appear in queries they are represented by the type ModelCode. A property has a domain, which is the set of resources to which it applies and a range, which is the set of values it can take. Associations between resources are created by properties whose range, like the domain, is a set of resources. For example, the location property might associate a switch with the substation in which it is located.

## Slide 3: GDA Concepts
PropertyValue
  A property value specifies a property by its resource identifier and its associated value for a given resource.
ResourceDescription
  The purpose of the DAF and GDA is to supply information about resources, or resource descriptions. A resource description gives a value for each of several properties of a given resource. The simplest resource description describes a single property and is made up of a resource identifier, a property identifier, and a property value. In Query service a resource description is represented by the type ResourceDescription.
ResourceDescriptionIterator
  Queries that return information about more than one resource return an iterator. The resource description iterator allows a client to access a large query result sequentially, several resources at a time.

## Slide 4: GDA Concepts
Association
  An association is a mapping from source set of resources to a destination set of resources. It contains a property and a class, each represented by their resource identifier. The interpretation of the property depends on the inverse member, a bool. In any case, the property range must be a resource, not a literal type. It may be single-valued or many-valued. An association may be evaluated in the context of a source resource to yield a set of zero or more destination resources.

## Slide 5: Resource Query Service - GetValues
  This method gets a resource description for an entity requested by the specified source id (resourceId).
public ResourceDescription GetValues(long modelVersionId,
long resourceId,
List<ModelCode> propIds,
ref int modelDeltaCounter)
  Usage:
  Input argument resourceId represents the identification of a requested resource. Input argument propIds contains the list of the properties that are returned with each results' instance.

## Slide 6: Resource Query Service - GetExtentValues
This method retrieves all instances of a given class, with specified properties.
public int GetExtentValues(long modelVersionId,
ModelCode code,
List<ModelCode> propIds, ref int modelDeltaCounter)
Input argument code contains the identifier of the resource class. Input argument propIds contains the list of the properties that are returned with each results' instance. The return value is iterator, pointing to the result set of the query.

## Slide 7: Resource Query Service – GetDescendentValues 1/2
This function retrieves all instances by a sequence of associations, which apply to a sequence of input source resource identifiers. For each association in association sequence, it is applied to each resource in the source sequence, yielding a new resource sequence. For example, a source resource sequence could be thought of as "all the substations in the model", and an association could be thought of as "all the bays in a substation", thus yielding a new sequence "all the bays in all the substations". This new sequence, obtained after applying the first association is then used as an entry to the next iteration of the process, which is applying the next association from the sequence. Once all associations have been applied to all the yielding sequences, a final sequence of all the leaf resources is obtained and returned to the client via ResourceIterator class.

## Slide 8: Resource Query Service – GetDescendentValues 2/2
public int GetDescendentValuesLinq(long modelVersionId,
List<ModelCode> propIds,
List<Association> path,
List<long> sources,
List<Association> tail,
ref int modelDeltaCounter)
Input argument propIds contains all the properties, for the final level of association sequence, that is, the properties that are to be returned for each leaf from the resulting sequence. path contains an ordered list of all the associations which will be applied to each level of sources sequence. sources contains a list of the first level source identifiers, which are used as a base for the entire query. This argument must contain the list of identifiers of instantiated objects (leafs) in the model, and not the class or type codes. Input argument tail contains a list of all the associations that could not yield any result (according to GDA specification).

## Slide 9: Filtered query service – GetFilteredExtentValues 1/2
This function retrieves instances of a given class, along with the specified properties, when a given filter is satisfied.
public int GetFilteredExtentValues(long modelVersionId,
ModelCode code,
List<ModelCode> propIds,
FilterNode fn,
ref int modelDeltaCounter)
Input argument code contains the identifier of the resource class. Input argument propIds contains the list of the properties that are returned with each results' instance. Input argument fn represents a filter node, and should contain a reference to a tree of filter nodes which all together represent a filter expression. A filter expression can be created directly, by creating filter nodes and adding them to a tree structure, or by using a FilterParser tool, that can parse through a simple filter expression.

## Slide 10: Filtered query service – GetFilteredExtentValues 2/2
Filter parser can be used to produce more complex filtering conditions, with multiple AND and OR conditions. For example a string like this:
"(SWITCH_TYPE = Breaker) AND (IDOBJ_GID >= 0123456789)
would be turned into appropriate filter expression tree.
All sub-expressions must be enclosed inside brackets.
Brackets balance and nesting is validated, and multiple brackets around single expression can also be used.